## Slide 1
Samantha Gandini
Nova Gorica – 13th November 2024
Example of application of LCA in green hydrogen production
* Image courtesy of Iren

## Slide 2
Broader Context
In this context, hydrogen plays a significant role in this transition due to its diverse applications, ranging from an alternative fuel to a carrier for transporting green energy.
Greenhouse gases are responsible for hold heat within the atmosphere and for this reason, they are accountable for climate changes. Greenhouse gases production is regulated by various legislations.
One of the sources affecting mainly GHG emissions is the energy sector. For this reason, governments are funding projects for the installation of renewables plants aimed at diversifying energy supplies.
10 million tonnes1
1 million tonnes2
45 %
300 b€
of renewables in the EU mix by 2030
founded by Recovery and Resilience Facility for RES
of hydrogen produced in EU and imported to EU by 2030
Oman’ target for hydrogen production by 2030
Source1: https://energy.ec.europa.eu/topics/energy-systems-integration/hydrogen_en
Source2: https://www.iea.org/reports/renewable-hydrogen-from-oman
Notes: Tecnologie atte a ridurre le emission di gas serra che sono regolamentati dalle seguenti legislazioni:
Conferenza nazioni unite sul clima  imposto il target del net zero entro il 2050 a cui poi si sono allineate tutte le nazioni negli anni successivi
In particolare

## Slide 3
Scope of the study
Evaluate from an environmental and economical point of view, differences between hydrogen import from MENA region to Italy and the domestic production in Italy.
Technical basis of design
LCA Analysis
Cost Analysis
RES plants capacity
Electricity production
Hydrogen production
Losses and boil-off
Available data gathering
LCA software
Emissions for 1 kg CO2 eq./kg H2
Losses and boil-off
CAPEX/OPEX identification
LCOE calculation
LCOH calculation for each process
Notes: Quantità diverse di idrogeno  mettere direttamente qui

## Slide 4
Hydrogen import from Oman
Hydrogen domestic production in Italy
Boil-off recirculation
Scenarios analysed
Renewable energy production
PV plant 700 MW
Wind plant 200 MW
Electrolysis
PEM 560 MW
Shipping
Ship 1500 ton
4.3 GWh/d
78.4 t H2/d
77.36 t H2 /d
75 t H2 /d
Liquefaction
80 ton/day
Storage
20 days storage
Storage
20 days storage
Regasification
Powered by Italian grid green electricity
Shipping
2 Trucks with 5 ton
1.5 GWh/d
22.1 t H2/d
21.7 t H2 /d
Storage
1 day storage
Storage
1 day storage
20 t H2 /d
Hydrogen production in Italy is four times lower than Oman scenario
Renewable energy production
PV plant 200 MW
Green electricity acquired by grid
Electrolysis
PEM 160 MW
Liquefaction
20 ton/day
Regasification
Powered by Italian grid green electricity
Notes: Quantità diverse di idrogeno  mettere direttamente qui

## Slide 5
Life Cycle Assessment (LCA)
Processes considered in the environmental analysis
RES plants
Photovoltaic plant construction
Wind plant construction
Hydropower plant construction
Electrolysis
Electrolyser construction
Electrolyser operation
Liquefaction
Liquefaction plant construction
Liquefaction plant operation
Storage
Storage tank construction
Regasification
Regasification plant construction
Regasification plant operation
Shipping
Ship:
Fuel consumption
Ship construction
Port facilities
Truck:
Fuel consumption
Truck construction
Road maintenance
Plant capacity
Panel efficiency
Irradiance
Plant capacity
Plant capacity
Tank capacity
No changes
Plant capacity

## Slide 6
Focusing on LCA
Software
Database
Interesting results

## Slide 7
Assumptions for cost analysis
Capital costs, multiplied for the capital recovery factor (CRF)
Operational & Maintenance costs (O&M)
Energy costs, evaluated by calculating the Levelized cost of electricity for both scenarios (LCOE)
Replacement costs (REPLEX), multiplied for a factor that included the replacement year
r is the discount rate and t is the lifetime horizon
Costs considered in the economic analysis
N.B. FFR = factor for replacement is not a common acronym but it has been used in this case to point at the CRF multiplied for a factor that considers the year of replacement
Sensitivity analysis
Land Costs
Discount rate variation
Variation in capital costs for installation of RES plants

## Slide 8
Power PV and wind plant
Electrolysis
Liquefaction
Liquefaction Losses
Electrolysis Losses
Storage
Shipping
Storage
Shipping boil-off gas
Storage boil-off gas
Regasification
Green electricity acquired by the grid at the final delivery point in Italy
Saved Electricity
83 %
10 %
6 %
60 %
54 %
54 %
50.3 %
50.1 %
50.1 %
H2
Losses among the supply chain
0.1 %
Power PV and grid
Electrolysis
Liquefaction
Electrolysis Losses
Storage
Shipping
Storage
Regasification
Green electricity acquired by the grid at the final delivery point in Italy
Saved Electricity
80 %
11 %
8.9 %
60 %
49 %
48.8 %
48.6 %
48.4 %
48.4 %
H2
0.1 %
boil-off gas
Oman scenario
Italy scenario
Shipping boil-off gas
Storage boil-off gas
Liquefaction Losses
Notes: Losses among the supply chain

## Slide 9
Life Cycle Assessment (LCA) Results
Chart: kg CO2-eq./kg H2
| Oman scenario | Italy scenario
Electrolysis | 2.03 | 1.73
Liquefaction | 0.29 | 0.24
Storage | 0.07 | 0.01
Transport | 0.15 | 0.1
Regasification | 0.06 | 0.05
2.60 kg CO2-eq./kg H2
2.13 kg CO2-eq./kg H2
Chart: 
| Electricity production, photovoltaic | Electricity production, wind | Electrolyser construction | Electrolyser BOP | Water deionized
Sales | 1.58 | 0.18 | 0.22 | 0.04 | 0.004
Carbon footprint of both scenarios (kg CO2-eq./kg H2)
Carbon footprint of electrolysis (kg CO2-eq./kg H2)

## Slide 10
Levelized Cost of Hydrogen (LCOH) Results
9.26 €/kg H2
8.56 €/kg H2
Chart: LCOH - variation Discount rate
| 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1 | 0.11
Oman | 9.65 | 10.21 | 10.79 | 11.39 | 12
Italy | 8.83 | 9.15 | 9.49 | 9.83 | 10.19
LCOH for both scenarios (€/kg H2 )
Sensitivity analysis
PV costs for installation:
Oman: 1300 €/kW
Italy: 970 €/kW
Notes: Acronimo da mettere lungo

## Slide 11
Considerations and Discussion
There are several factors to be considered in order to evaluate properly the results of the analysis:
1
Uncertainties in LCA and costs assumed data
2
Different quantities of hydrogen produced and transported between scenarios
27 kton/year in Oman scenario
7.3 kton/year in Italy scenario
3
Hydrogen could be used directly on the production site in Italy scenario
1.74 kg CO2-eq./kg H2
7.73 €/kg H2
LCA
Economic
Notes: Uncertainties in LCA data due to:
  Unavailability of similar hydrogen processes  e.g. storage and transportation processes did not include materials for cryogenics liquids
  Impacts of locations  e.g. water from desalinization plants in Oman has an impact of 5-6 kg CO2/m3 while in Italy of 0.30 kg CO2/m3
Economic analysis:
  Uncertainties in cost estimation related to hydrogen processes such as liquefaction and regasification processes that have been estimated on LNG bases or limited hydrogen plants available
  Lack of data related to locations

## Slide 12
Digital models for H2 distribution
Thank you
Samantha Gandini
samantha.gandini@studenti.units.it
Image credits: elaborated from https://www.ufihydrogen.com/it/